The Typewriter Repairmen

2011 National Underwater Robotics Challenge

Technical Report

June 3, 2011

Tucson, Chandler, and Sierra Vista, AZ

Adult Team

selectric.org/nurc11

Team Members:

Jim Forbes

David Forbes

Janet Forbes

Steven Forbes

Kevin Forbes

Gary Forbes

Katie Roch

Table of Contents

Abstract	3

Team Goal	3

Mission Analysis	3

Existing ROV Systems	4

ROV Modifications	6

Software	9

Testing	10

New skills	11

Lessons Learned	12

Acknowledgements	12

Original Bill of Materials	12

2011 Bill of Materials	16

References	17

# Abstract

The Typewriter Repairmen is a family adult team. Several team members have vast experience in high school robotics, both with FIRST and NURC. This is the team's third year of competition in NURC.

Our goal this year is to get a good score, while doing as little work as possible. We have decided to reuse both our previous ROVs instead of building another. We spent a few days making some modifications to the ROVs and testing these modifications. We also took time to make mission props and test our ability to perform some of the more difficult maneuvers in the mission.

# Team Goal

The Typewriter Repairmen is a family team. Our goal is to have fun and enjoy each other’s company while doing a very good job of completing the requirements of the NURC competition and sharing our experiences with the other teams.

# Mission Analysis

We built a spreadsheet of the mission tasks, estimated execution time, and point rewards to create a ranked list of the reward/effort ratio for each task. The tasks have a two-to-one range of points/minute. Based on this spreadsheet, we have decided to attempt to perform all tasks in the mission, although we have not devoted much time to building special robot hardware for each task. We did have to modify the ROVs to accomplish some of the tasks.

# Existing ROV Systems

The Typewriter Repairmen currently have two complete ROV systems. NotBob, the yellow ROV, was built for the 2009 NURC competition “Mount Terror: Fire Under the Ice”. Babs, the red ROV, was built for the 2010 competition “Nessie Quest”. Both ROVs have a steel strap frame and a cylindrical electronics housing. Thrust is by bilge pump motors with ducted propellers. The ROV electronics consist of custom designed hardware.

NotBob was a radical departure from typical competition ROV designs. His design was based on systems engineering principles, combined with novel design concepts. The vision system includes a tilting camera, giving him excellent vision over a wide area . The electronics and camera enclosure is sealed with O rings to prevent leaks and provide easy service access. The electronics system was custom designed and built just for use in an ROV. The chassis is made of steel, which is easy to fabricate and cost effective.

Babs is a refinement of notBob. She has most of the same features, with some improvements. The electronics enclosure wiring is all sealed with individual O rings, which are easy to use, inexpensive, and provide excellent sealing (we have never found even a drop of water inside). The electronics is smaller, more capable, and can be reconfigured during operation. There are more thrusters and a lighter chassis for improved speed.

# ROV Modifications

Since we are using two ROVs that we had built in previous years, the 2011 build process consisted of modifying these ROVs.

Since both ROVs are still in good working order, we decided that we would use both of them in the mission to increase our chances of completing all tasks in the allotted time. We did feel that some modifications to Babs to improve her maneuverability were needed, so that she would be able to place the life forms in the shallow specimen holding tank.

Babs

Babs is a very capable little ROV. She has six drive motors (two fore-aft, three lift/dive/pitch, one strafe) for ample thrust in every direction. Her control system is versatile and easy to drive and configure. Her manipulator claw both grips and rotates. We saw no reason not to use her again this year, although we knew she would need some modification to complete the mission. The main issue was the need to be able to reach up with her claw.

We spent quite a bit of time exploring ways to build a new rotating arm/claw assembly. None of the concepts we thought of looked easy to build. We finally realized that we could probably get away with simply modifying Babs to be able to reach up with her existing claw. This plan would require reducing her stability, to increase her existing tilting ability. ROV stability is a result of having the center of buoyancy higher than the center of mass.

Babs required a bit of frame and float modification to reduce her stability enough to improve her ability to pitch fore and aft on command. The original floats were two 1-liter stainless steel cans of 10cm diameter. The float cans have been replaced with a hollow, 12 x 18 x 18 cm block of syntactic foam - a mixture of glass microspheres and polyester resin, as used to make lightweight fiberglass structures such as aircraft. The advantage of syntactic foam over the cans is that it can be formed into any shape desired. In this case, the cube of foam is placed at the rear center of the frame.

Using the syntactic foam float allowed us to move the two fore-aft thrusters back inside the frame edge, making Babs narrower. The new flotation system allowed us to relocate some of the ballast to a higher, more forward location. This gives her better maneuverability as well, allowing the differential vertical thrusters to hold Babs in a pitched attitude from full-face-down to full-face-up with little effort.

An opposite pitch propeller was built to permit the two fore-aft thrusters to be counter-rotating, thereby eliminating rolling torque reaction.

The torpedo launching system and laser sight used for the 2010 mission were removed from Babs to save weight.

No changes were made to the electronics portion of either ROV, as they perform all needed tasks and are fully functional. However, a second battery box was needed to allow both ROVs to operate at the same time. The original 48V battery box was duplicated, but using a slightly larger toolbox to allow storage of the controller, transmitter and associated cables inside the box. Each battery box has four 12V 7AH lead-acid batteries, and a set of four center-off toggle switches to enable solar charging in parallel and ROV operation in series. The new box also includes a digital panel voltmeter, to monitor charging voltage, and allow quick checks of the voltage of each battery.

The solar charging systems work very well, and we continue to use only solar power to charge the ROV batteries. The batteries and solar charging system are also used at the Burning Man festival each fall.

# Software

NotBob

One problem we encountered was that we designed NotBob to use two vEx remote transmitters, requiring two ROV operators for a single ROV. Our experience with Babs last year having a single operator was more effective, so we decided to see if we could change notBob to use a single controller. We figured out that by using a USB gamepad, an Arduino microcontroller board, a netbook, and some publicly available software, we could create a new control system with the same control configuration as Babs.

A python script communicates with a Logitech Gamepad, using the laptop's larger computing power to determine motor speeds and run control loops. Since python is an interpreted language, deployment time for code fixes is reduced drastically. The Arduino acts as a signal relay, converting USB serial information into modulated pulses. Each vEx transmitter has 6 channels; each pulse starts with a 400 microsecond low signal, followed by a 700 to 1500 microsecond high pulse. The Arduino converts serial data from the laptop into simulated vEx transmitter pulse delays while sending back analog readings from the depth sensor. An optional PID loop can be engaged, maintaining NotBob's current depth to ease complicated driving maneuvers. The control system physically contains the same number of parts, but is generally smaller; two transmitters have been replaced with a laptop and gamepad, while the Hello Kitty Command Console has been modified to hold the Arduino.

# Testing

The 2011 mission requires the ROV to capture a life form and place it in a specimen holding tank. We built a prop of the bobbing life form in order to test our ability to perform these tasks. Rather than make a complete motorized unit like the actual mission props, we made a simpler passive life form with positive buoyancy.

We attached a length of fishing line to the prop, running the fishing line through a pulley attached to a brick placed at the bottom of the test pool. Pulling on the fishing line causes the prop to move up and down in the pool.

We tested our ability to place it in the specimen holding tank by simulating the edge of the tank with a piece of PVC pipe held 10cm under the water surface by two team members.

# New skills

The Typewriter Repairmen look forward to the build season as an opportunity to expand their skill set. This season provided the chance to learn how to make syntactic foam using polyester resin and microspheres as a filler. Searching the internet revealed very little information about making syntactic foam. There were a few hints, but no “how to” articles. We decided to buy some materials, and experiment. There are a few online stores that sell composite materials, so we purchased two gallons of microspheres for filler. Polyester resin is available locally at building supply stores and auto paint stores. Online research indicated the best approach would be mixing the resin with its catalyst first, then adding a third of the filler at a time, mixing thoroughly at each step. The unknown was the ratio of resin to filler. Our experiments showed that a volume ratio of between three and four parts filler to one part resin was about right. Less filler leaves a runny mixture, and more filler makes it too stiff to mix and work with.

The creation of a new control system for NotBob provided the opportunity to play with an Arduino controller and to build an application in Python.

# Lessons Learned

We encountered a problem with the foam block while testing Babs. One corner of the foam began to take on water. The resin apparently hadn’t been mixed thoroughly, causing the foam to be hydroscopic. To repair the block, we cut off the defective corner of the block and applied a patch, taking care to mix the resin thoroughly.

This control system has been implemented in the Python language, chosen for its ease of use and fast edit-test cycle. Unfortunately, the platform on which Python is running is Windows 7, which is less than ideal due to its ability to run so many various applications, and it’s almost infinite configurability. When the computer hibernates, the Python interpreter gets into a bad state, from which the only recourse is a power cycle. The simple solution is to close the Python application before putting the computer into the hibernation state.

# Acknowledgements

The Typewriter Repairmen would like to thank the Malmbergs and the Jones for the generous use of their swimming pools for robot testing.

We would also like to thank APASE, and the judges and other volunteers, for their hard work in putting on this competition.

# Original Bill of Materials

NotBob

| Section | Part | Material | Source | Unit Cost | Quantity | Total Cost | Actual |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Electronics | Board | Aluminum 1/4" x 4" x 8" | Online Metals | $ 6.70 | 1 | $ 6.70 | $ - |
| Electronics | Board Mount | Aluminum Angle 1/16" x 1/2" | Ace | $ 4.79 | 1 | $ 4.79 | $ 4.79 |
| Electronics | Cables | Epoxy Plastic Slow Set | Ace | $ 3.49 | 1 | $ 3.49 | $ 3.49 |
| Electronics | Velcro | Industrial 2" x 4' Black | Ace | $ 10.99 | 1 | $ 10.99 | $ 10.99 |
| Electronics | Connector | Bulgin 2 pin male cable | Digi-Key | $ 12.10 | 4 | $ 48.40 | $ 48.40 |
| Electronics | Connector | Bulgin 2 pin female cable | Digi-Key | $ 10.05 | 1 | $ 10.05 | $ 10.05 |
| Electronics | Connector | Bulgin 2 pin male panel | Digi-Key | $ 11.56 | 1 | $ 11.56 | $ 11.56 |
| Electronics | Connector | Bulgin 2 pin female panel | Digi-Key | $ 10.34 | 4 | $ 41.36 | $ 41.36 |
| Electronics | Connector | Bulgin 6 pin female cable | Digi-Key | $ 11.99 | 1 | $ 11.99 | $ 11.99 |
| Electronics | Connector | Bulgin 6 pin male panel | Digi-Key | $ 14.16 | 1 | $ 14.16 | $ 14.16 |
| Electronics | Connector | Bulgin 9 pin male cable | Digi-Key | $ 10.90 | 1 | $ 10.90 | $ 10.90 |
| Electronics | Connector | Bulgin 9 pin female cable | Digi-Key | $ 10.90 | 1 | $ 10.90 | $ 10.90 |
| Electronics | Connector | Bulgin 9 pin male panel | Digi-Key | $ 12.51 | 1 | $ 12.51 | $ 12.51 |
| Electronics | Connector | Bulgin 9 pin female panel | Digi-Key | $ 12.42 | 1 | $ 12.42 | $ 12.42 |
| Electronics | Controller | ESC4A Speed Controller Board | Cathode Corner | $ 150.00 | 2 | $ 300.00 | $ 300.00 |
| Electronics | Controller | vEx Transmitter | vexrobotics | $ 129.99 | 2 | $ 259.98 | $ - |
| Electronics | Case | Hello Kitty lunch box | Target | $ 9.99 | 1 | $ 9.99 | $ 9.99 |
| Electronics | Case | Zero Aluminum Case 18x24x7.5 | Cases2Go | $ 450.00 | 1 | $ 450.00 | $ - |
| Electronics | Case | Zero Aluminum Case 18x13x5 | Cases2Go | $ 350.00 | 1 | $ 350.00 | $ - |
| Electronics | Connector | Molex Jr 8 pin pair | Digi-Key | $ 4.25 | 2 | $ 8.50 | $ 8.50 |
| Electronics | Connector | Molex Jr 6 pin pair | Digi-Key | $ 3.45 | 1 | $ 3.45 | $ 3.45 |
| Electronics | Connector | Molex Jr 2 pin pair | Digi-Key | $ 1.85 | 3 | $ 5.55 | $ 5.55 |
| Electronics | Connector | Bulgin Gland Pack | Digi-Key | $ 1.04 | 8 | $ 8.32 | $ 8.32 |
| Electronics | Connector | Bulgin Cap Plug | Digi-Key | $ 1.48 | 6 | $ 8.88 | $ 8.88 |
| Electronics | Connector | Bulgin Cap Socket | Digi-Key | $ 1.14 | 6 | $ 6.84 | $ 6.84 |
| Float | Tube | 3" ABS Sewer Pipe | Lowes | $ 4.02 | 1 | $ 4.02 | $ 4.02 |
| Float | End cap | ABS end cap | Sutherlands | $ 4.79 | 4 | $ 19.16 | $ 19.16 |
| Float | Clamp | Hose Clamp #64 | Lowes | $ 1.53 | 4 | $ 6.12 | $ 6.12 |
| Float | Valve | 1/4" petcock | Home Depot | $ 2.51 | 2 | $ 5.02 | $ 5.02 |
| Frame | Skids | Steel rod 1" x 36" | Aztec Welding | $ 3.20 | 2 | $ 6.40 | $ 6.40 |
| Frame | Else | Steel strap 1/2" x 1/8" | Aztec Welding | $ 8.04 | 1 | $ 8.04 | $ 8.04 |
| Gimbal | Structure | Aluminum Sheet 5052 0.050" | Online Metals | $ 22.56 | 1 | $ 22.56 | $ 22.56 |
| Gimbal | Servo | Metal Gear Servo HRC32225S | Hobbytown | $ 33.50 | 1 | $ 33.50 | $ 33.50 |
| Gimbal | Camera | Color Security Camera | Radio Shack | $ 29.99 | 2 | $ 59.98 | $ 59.98 |
| Gimbal | Light | Halogen 20W MR16 Flood bulb | Lowes | $ 5.98 | 1 | $ 5.98 | $ 5.98 |
| Gimbal | Light | Luxeon LED 3W 5 pack | cece718 | $ 17.97 | 1 | $ 17.97 | $ 17.97 |
| Gimbal | Light Socket | GX 5.3 Bipin Lampholder 2 pack | hamizoh | $ 4.99 | 1 | $ 4.99 | $ 4.99 |
| Manipulator | Motor | Rule 500 Bilge Pump | Amazon | $ 18.88 | 1 | $ 18.88 | $ 18.88 |
| Manipulator | Sliders | Cutting Board HDPE | WalMart | $ 1.97 | 1 | $ 1.97 | $ 1.97 |
| Manipulator | Arms | Alum Channel 3/8" x 1/2" x 1/16" | Ace | $ 7.99 | 1 | $ 7.99 | $ 7.99 |
| Manipulator | Arms | Alum Channel 5/8" x 1/2" x 1/16" | Ace | $ 8.49 | 1 | $ 8.49 | $ 8.49 |
| Manipulator | Screw | Threaded Rod 1/4-28 | Ace | $ 1.99 | 1 | $ 1.99 | $ 1.99 |
| Manipulator | Grip | Mouse Pad | SWS | $ 2.50 | 1 | $ 2.50 | $ 2.50 |
| Manipulator | Basket | Bath Chrome | Target | $ 9.99 | 1 | $ 9.99 | $ 9.99 |
| Paint | Red | Krylon Banner Red 12oz can | WalMart | $ 2.97 | 1 | $ 2.97 | $ 2.97 |
| Paint | Yellow | Krylon Sun Yellow 12oz can | WalMart | $ 2.97 | 3 | $ 8.91 | $ 8.91 |
| Power | Switch | DPDT 20A Center Off | Radio Shack | $ 3.99 | 4 | $ 15.96 | $ 15.96 |
| Power | Connector | Anderson Power 4pk | Elliott | $ 3.81 | 3 | $ 11.43 | $ 11.43 |
| Power | Fuse | 10 A Blade 3 pk | Radio Shack | $ 1.99 | 1 | $ 1.99 | $ 1.99 |
| Power | Enclosure | Tool Box, Plastic 17800 | techni-tool | $ 21.05 | 1 | $ 21.05 | $ - |
| Power | Panel | BP 75 W Solar Panel | Affordable Solar | $ 391.00 | 1 | $ 391.00 | $ - |
| Power | Controller | Morningstar SunSaver10 Charger | Affordable Solar | $ 48.00 | 1 | $ 48.00 | $ - |
| Power | Wire | 18 gage red/black zip 8m | Radio Shack | $ 5.99 | 1 | $ 5.99 | $ 5.99 |
| Power | Batteries | SLA 12v 7ah rechargeable | Radio Shack | $ 34.99 | 4 | $ 139.96 | $ - |
| SCULL | End Plugs | Aluminum Plate 1/2" x 4" x 36" | McMaster Carr | $ 55.86 | 1 | $ 55.86 | $ 55.86 |
| SCULL | Tube | Polycarbonate Tube 6"x1/8"x12" | McMaster Carr | $ 33.22 | 1 | $ 33.22 | $ 33.22 |
| SCULL | O ring | 254 O ring EPDM 10 pack | McMaster Carr | $ 9.30 | 1 | $ 9.30 | $ 9.30 |
| Sensor | Thermometer | Acu-Rite | WalMart | $ 12.00 | 1 | $ 12.00 | $ 12.00 |
| Sensor | Pressure | MPXA4250AC6U | Digi-Key | $ 14.96 | 1 | $ 14.96 | $ 14.96 |
| Tether | Power | Speaker Wire #16 x 2 | SWS | $ 25.00 | 1 | $ 25.00 | $ 25.00 |
| Tether | Signal | Cat5 Network Cable | SWS | $ 40.00 | 1 | $ 40.00 | $ 40.00 |
| Tether | Float | Foam Backer Rod 9mm x 6m | Ace | $ 4.49 | 1 | $ 4.49 | $ 4.49 |
| Tether | Connector | Jack Phone Duplex | Sutherlands | $ 2.79 | 1 | $ 2.79 | $ 2.79 |
| Tether | Connector | Phone Handset Plug 10 pk | Elliott | $ 1.69 | 1 | $ 1.69 | $ 1.69 |
| Tether | Connector | RCA Jack 4 place | Elliott | $ 1.50 | 2 | $ 3.00 | $ 3.00 |
| Thruster | Propeller | 3 blade 75mm d 50mm p Right | Dumas | $ 33.75 | 2 | $ 67.50 | $ 67.50 |
| Thruster | Propeller | 3 blade 75mm d 50mm p Left | Dumas | $ 33.75 | 1 | $ 33.75 | $ 33.75 |
| Thruster | Propeller | 3 blade 62mm d 50mm p Right | Dumas | $ 28.00 | 1 | $ 28.00 | $ 28.00 |
| Thruster | Motor | Rule 1100 Bilge Pump | Amazon | $ 31.05 | 3 | $ 93.15 | $ 93.15 |
| Thruster | Motor | Rule 500 Bilge Pump | Amazon | $ 18.88 | 1 | $ 18.88 | $ 18.88 |
| Thruster | Clamp | Hose Clamp #20 2 pack | Lowes | $ 1.83 | 2 | $ 3.66 | $ 3.66 |
| Thruster | Shaft | 3/8" aluminum rod 3' | Online Metals | $ 1.92 | 1 | $ 1.92 | $ - |
| Thruster | Nozzle | 3" ABS Sewer Pipe | Lowes | $ 4.02 | 1 | $ 4.02 | $ 4.02 |
|  |  |  | LIST TOTAL: | $ 2,967.73 |  |
|  |  |  | ACTUAL TOTAL: |  | $ 1,299.12 |

Babs

| Section | Part | Material | Source | Total Cost |
| --- | --- | --- | --- | --- |
| Electronics | Connector | DE 9 pin connectors | Elliott | $ 2.00 |
| Electronics | Connector | Molex 8 pin KK shells | Digi-Key | $ 2.65 |
| Electronics | Connector | Molex pins | Digi-Key | $ 2.00 |
| Electronics | Controller | Sony Play Station 2 | WalMart | $ 20.00 |
| Electronics | Controller | RSCA Dual Speed Controller | Cathode Corner | $ 308.76 |
| Electronics | Controller | RTX ROVotron Transmitter | Cathode Corner | $ 128.13 |
| Electronics | Controller | RRX ROVotron Receiver | Cathode Corner | $ 105.72 |
| Electronics | Controller | Card cage metalwork | Precision Tool | $ 175.00 |
| Electronics | Seal | 104 O Ring | McMaster Carr | $ 4.82 |
| Electronics | Torpedo | Capacitor 2200uf 63V | Digi-Key | $ 3.41 |
| Electronics | Velcro | Industrial 2" x 4' Black | Ace | $ 10.99 |
| Float | Clamp | Hose Clamp Stainless #72 | Lowes | $ 3.66 |
| Float | End cap | UHMW Plastic 1/2" thick | McMaster Carr | $ 13.10 |
| Float | O ring | EPDM 245 16 pk | McMaster Carr | $ 9.56 |
| Float | Tube | 2 Qt Storage Container | WalMart | $ 13.94 |
| Frame | Paint | Krylon Banner Red 12oz can | WalMart | $ 2.97 |
| Frame | Structure | Steel strap 1/2" x 1/8" | Aztec Welding | $ 2.40 |
| Gimbal | Base | Aluminum 3/16" x 4" x 4" | Online Metals | $ 13.97 |
| Gimbal | Camera | Defender 82-12836 color camera | MCM Electronics | $ 89.99 |
| Gimbal | Light | Luxeon LED 3W Star White | Dan Bolin | $ 14.40 |
| Gimbal | Pivot | Spring, wave, 26mm ID | McMaster-Carr | $ 0.42 |
| Gimbal | Servo | HiTec HS-645MG | Hobbytown USA | $ 39.50 |
| Gimbal | Structure | Aluminum Sheet 5052 0.050" | Online Metals | $ 4.19 |
| Gimbal | Top | Polycarbonate Sheet 1/8"x6"x12" | McMaster Carr | $ 6.64 |
| Manipulator | Arms | Polycarbonate Sheet 1/8"x6"x12" | McMaster Carr | $ 6.64 |
| Manipulator | Body | UHMW Plastic 1-1/2" x 1" | McMaster Carr | $ 6.70 |
| Manipulator | Hoops | Brass Rod 1/8" | Lowes | $ 2.17 |
| Manipulator | Motor | Rule 1100 Bilge Pump | Amazon | $ 73.44 |
| Manipulator | Screw | Aluminum Rod 1/2" | Ace | $ 4.49 |
| Manipulator | Spacer | Aluminum Rod 1/4" | Ace | $ 2.99 |
| Manipulator | String | Monfilament 20# | WalMart | $ 2.50 |
| Power | Batteries | SLA 12v 7ah rechargeable | Radio Shack | $ 139.96 |
| Power | Connector | Anderson Power 4pk | Elliott | $ 11.43 |
| Power | Controller | Morningstar SunSaver10 Charger | Affordable Solar | $ 48.00 |
| Power | Enclosure | Tool Box, Plastic 17800 | techni-tool | $ 21.05 |
| Power | Fuse | 10 A Blade 3 pk | Radio Shack | $ 1.99 |
| Power | Panel | 40 W Solar Panel | UL Solar | $ 78.84 |
| Power | Switch | DPDT 20A Center Off | Radio Shack | $ 15.96 |
| Power | Wire | 18 gage red/black zip 8m | Radio Shack | $ 5.99 |
| SCULL | End Plugs | Aluminum Plate 1/2" x 6" x 12" | Online Metals | $ 16.32 |
| SCULL | O ring | EPDM 253 10 pack | McMaster Carr | $ 9.27 |
| SCULL | Tube | Polycarbonate Tube 6"x1/8"x12" | McMaster Carr | $ 33.22 |
| Sensor | Pressure | MPXA4250AC6U | Digi-Key | $ 14.96 |
| Tether | Float | Foam Backer Rod 7mm x 6m | DKHardware | $ 15.80 |
| Tether | Power | Speaker Wire #16 x 2 | HomeDepot | $ 23.51 |
| Tether | Signal | Cat5 Network Cable | SWS | $ 25.00 |
| Thruster | Clamp | 1-1/2" Steel Tube 16 ga | Aztec Welding | $ 1.38 |
| Thruster | Motor | Rule 1100 Bilge Pump | Amazon | $ 187.38 |
| Thruster | Prop Blade | 0.032" x 1" x 12" Brass | Ace | $ 5.97 |
| Thruster | Prop Hub | 1/4"-28 Brass Nut | Sutherlands | $ 0.90 |
| Thruster | Shaft | Aluminum Rod 3/8" | Ace | $ 6.99 |
| Thruster | Shroud | 3" Steel Tube 16 ga | McMaster Carr | $ 36.62 |
| Thruster | Support | 1/8" Steel Rod | Lowes | $ 2.58 |
| Torpedo | Battery | 2CR5 | WalMart | $ 29.88 |
| Torpedo | Controller | PC Board, bare | Advanced Ckts | $ 24.00 |
| Torpedo | Controller | PC board components | Digikey | $ 19.50 |
| Torpedo | Ends | 1-1/2" UHMW Rod | McMaster Carr | $ 3.36 |
| Torpedo | Housing | 1-1/2" Polycarbonate Tube | McMaster Carr | $ 11.37 |
| Torpedo | Launcher | Solenoid, lawn sprinkler | Ace | $ 12.45 |
| Torpedo | Magnet | 1/2" x 1/4" Rare Earth | McMaster-Carr | $ 20.76 |
| Torpedo | Motor | 6v 4350 RPM | AmSciSurplus | $ 2.97 |
| Torpedo | Nose | UHMW Plastic 1/2" thick | McMaster Carr | $ 6.55 |
| Torpedo | O ring | EPDM 123 25 pk | McMaster Carr | $ 7.85 |
| Torpedo | Payload | Plastic Tube 7/8" x 36" | Aztec Welding | $ 9.99 |
| Torpedo | Shaft | Aluminum Rod 3/16" | Ace | $ 1.39 |
| Torpedo | Support | Aluminum Strap 1/16" x 3/4" | Ace | $ 6.99 |
|  |  |  | TOTAL: | $ 1,937.33 |

# 2011 Bill of Materials

# References

3M Microspheres Selection Guide, 3M Company, www.3m.com

Evercoat Polyester Resin, Evercoat Company, www.evercoat.com

Subsea Void Filler SF-38, Engineered Syntactics Systems, www.esyntactic.com

Arduino C-based programming compiler and downloader,   www.arduino.cc

Python 2.7,  www.python.org

Gamepad interface library,   www.pygame.org

USB interface to Arduino,  pyusb.sourceforge.net

Technical Report, 2009 NURC ROV: notBob, The Typewriter Repairmen

Technical Report, 2010 NURC ROV: Babs, The Typewriter Repairmen

# Text boxes

| Section | Part | Material | Source | Unit Cost | Quanity | Total Cost |
| --- | --- | --- | --- | --- | --- | --- |
| Float | Float | Glass Microspheres | Infinity | $ 14.99 | 2 | $ 29.98 |
| Float | Float | Resin | Lowes | $ 17.49 | 2 | $ 34.98 |
| Float | Float | Plastic Filler | M&M Paint | $ 21.56 | 1 | $ 21.56 |
| Float | Retainer | Aluminum 1/8" x 1/2" x 4" | Ace | $ 4.99 | 1 | $ 4.99 |
| Frame | Paint | Krylon Banner Red 12oz can | WalMart | $ 2.97 | 2 | $ 5.94 |
| Power | Batteries | SLA 12v 7ah rechargeable | iii | $ 14.99 | 4 | $ 59.96 |
| Power | Connector | Anderson Power 4pk | Elliott | $ 3.81 | 1 | $ 3.81 |
| Power | Controller | Morningstar SunSaver6 Charger | Affordable Solar | $ 48.00 | 1 | $ 48.00 |
| Power | Enclosure | Tool Box, Plano | Plano | $ 21.05 | 1 | $ 21.05 |
| Power | Fuse | 10 A Blade 3 pk | Radio Shack | $ 1.99 | 1 | $ 1.99 |
| Power | Meter | 3 digit LED Panel Meter | ebay | $ 14.99 | 1 | $ 14.99 |
| Power | Switch | DPDT 20A Center Off | Radio Shack | $ 3.99 | 4 | $ 15.96 |
| Power | Wire | 18 gage red/black zip 8m | Radio Shack | $ 5.99 | 1 | $ 5.99 |
|  |  |  |  |  |  | $ - |
| Control | Arduino | Uno Circuit Board | Sparkfun | $ 29.95 | 1 | $ 29.95 |
| Control | Computer | Acer Aspire One | Walmart | $ 248.00 | 1 | $ 248.00 |
| Control | Gamepad | Logitech Gamepad | Target | $ 19.98 | 1 | $ 19.98 |
|  |  |  |  |  |  | $ - |
|  |  |  |  | TOTAL= |  | $ 567.13 |